## Slide 1
THERMAL GRU · ARCHITECTURE
Eliminating Cold-Start
with InitStateEncoder
From zero-initialised hidden state to physics-informed GRU initialisation
Thermal Prediction Research · GRU Model Improvement

## Slide 2
The Problem: Cold-Start with Zero Initialisation
def init_hidden(self, batch_size):
return torch.zeros(
self.num_layers,
batch_size,
self.hidden_size
)
⚠ h₀ = all zeros — no physical knowledge
t = 0
t = 30s
t = 14400s
Burn-in
(30 steps)
Reliable predictions
No prediction
for first 300s
Real-time feedback
requirement violated
Root Cause
①
GRU hidden state h₀ = zeros has no information about the physical system
②
Model needs 30 timesteps of real input to 'warm up' the hidden state to a meaningful value
③
Predictions during warm-up are unreliable — violating the real-time feedback requirement

## Slide 3
Solution: InitStateEncoder — Architecture Overview
Initial Condition
t = 0
T_outer (C)
T_inner (C)
T_avg (C)
Input Temp (C)
4 values
InitStateEncoder
Linear(4 → 256)
ReLU
Linear(256 → 256)
ReLU
Linear(256 → 640)
640-d
Reshape
[5, B, 128]
h₀
ThermalGRU
5 layers
hidden = 128
input = 4
output = 3
T_inner / T_outer / T_avg
InitStateEncoder + GRU are trained end-to-end via backpropagation — no separate pre-training required
Key Code Changes
① init_hidden() now accepts x0 parameter and routes through InitStateEncoder instead of torch.zeros()
② Dataset stores init_conditions (t=0 values) and passes them through the DataLoader
③ Burn-in loop (30 steps) removed entirely from both training and inference

## Slide 4
Before vs After: Data Flow Comparison
BEFORE (Zero Init + Burn-in)
h₀ = torch.zeros(...)
Burn-in: feed 30 real steps
(no loss computed)
Training starts at step 30
(first 30 steps wasted)
Inference: predict only
from step 30 onwards
AFTER (InitStateEncoder)
x₀ = [T_outer, T_inner,
T_avg, Input_T] at t=0
InitStateEncoder(x₀)
→ meaningful h₀
Training starts at step 0
(all 1440 steps used)
Inference: predict from
step 0 — no gap
vs

## Slide 5
Why It Works: Physical Intuition
t=0 is fully observable
At the first timestep, all four temperatures are known real measurements — T_outer, T_inner, T_avg and Input Temperature. This is complete physical state information.
h₀ encodes physical state
The encoder learns which hidden-state values allow the GRU to best predict subsequent temperatures. It implicitly learns thermodynamic relationships without explicit equations.
End-to-end gradient flow
Because encoder + GRU are jointly trained, the encoder receives gradients from every prediction step. It is directly optimised to minimise prediction error from t=0 onwards.
Result
✓ Prediction quality from step 0 matches mid-sequence quality — no cold-start degradation
✓ 30 extra training steps per sequence contribute to loss, improving overall model accuracy
✓ Real-time feedback requirement satisfied: users receive predictions immediately at system start
✓ Mean MAE T_inner: 1.6736 °C, Mean MAE T_outer: 1.9888 °C, Mean MAE T_avg: 1.9298 °C